## Slide 1: CPS 590: Software Defined Networking
Theophilus Benson

## Slide 2: Welcome!

## Slide 3: Administrative Details
Course Format
  Student Engagement (30%)
    Class Participation (20%)
    Paper Reviews (10%)
  Course Assignments (20%)
    Learning to use SDN environments
    Writing Controller Applications
  Course Project (60%)
    Deep dive into an SDN topic

## Slide 4: Outline
Section 1: SDN Ecosystem
  SDN Motivation
  SDN Primer
  Dimensions of SDN Environments
  Dimensions of SDN Applications
Section 2: OpenFlow Primer
Section 3: Demo/Use-cases
  Network Virtualization
Section 4: SDN Challenges
  SDN Challenges

## Slide 5: Section 1

## Slide 6: Network Today…
Vertical integrated stacks
  Similar to PC in 1980s
IBM’s Mainframe
Cisco Routers
D.B.
O.S
CPU
COBOL Apps.
VLANS
Switch O.S.
ASIC
L3 Routing

## Slide 7: Implications of Networking…
Restricted to ill defined vendor CLI
  Provisioning is slow….
    VM provisioning: 1min
    Virtual network provisioning: 1-3 weeks

## Slide 8: Background: Switch Internals
Logical View of a Switch
Physical Architecture of a Switch
Switching
Fabric
Processor
ASIC
AISC
data plane
control plane
Network O.S.
ASIC
Applications
Applications

## Slide 9: Software Defined Networking
Southbound API: decouples the switch hardware from control function
  Data plane from control plane
Switch Operating System: exposes switch hardware primitives
Network O.S.
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware
Network O.S.
ASIC
Applications
Applications
Current Switch
Vertical stack
SDN Switch
Decoupled stack

## Slide 10: Implications Of SDN
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Global View
Programmatic
Control
Current Networking
SDN Enabled Environment
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications

## Slide 11: Implications Of SDN
Current Networking
SDN Enabled Environment
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Distributed protocols
  Each switch has a brain
  Hard to achieve optimal solution
Network configured indirectly
  Configure protocols
  Hope protocols converge
Global view of the network
  Applications can achieve optimal
Southbound API gives fine grained control over switch
  Network configured directly
  Allows automation
  Allows definition of new interfaces
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications

## Slide 12: How SDN Works
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch H.W
Switch O.S
Switch H.W
Switch O.S

## Slide 13: How to Pick an SDN Environment
Network O.S.
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware
What is the Southbound AP!?
Is the switch hardware and OS closed?
Is the switch virtual or physical?
How easy is it to develop on for the
Controller platform?

## Slide 14: The SDN Stack
Controller
NOX
Slicing
Software
FlowVisor
FlowVisor
Console
14
Applications
LAVI
ENVI (GUI)
…
n-Casting
NetFPGA
Software
Ref. Switch
Broadcom
Ref. Switch
OpenWRT
PCEngine WiFi AP
Commercial Switches
OpenFlow
Switches
…
Monitoring/ debugging tools
oflops
oftrace
openseer
Open vSwitch
HP, IBM, NEC, Pronto, Juniper.. and many more
Beacon
Trema
FloodLight
Source: SDN Tutorial by B. Heller
Open Networking Summit, April 2012
Notes: There are components at different levels that work together in making it work

## Slide 15: Dimensions of SDN Environments: Vendor Devices
Vertical Stacks
Vendor bundles switch and switch OS
  Restricted to vendor OS and vendor interface
Low operational overhead
  One stop shop
Whitebox Networking
Vendor provides hardware with no switch OS
Switch OS provided by third party
  Flexibility in picking OS
High operational overhead
  Must deal with multiple vendors

## Slide 16: Dimensions of SDN Environments: Switch Hardware
Virtual: Overlay
Pure software implementation
  Assumes programmable virtual switches
  Run in Hypervisor or in the OS
  Larger Flow Table entries (more memory and CPU)
Backward compatible
  Physical switches run traditional protocols
Traffic sent in tunnels
  Lack of visibility into physical network
Physical: Underlay
Fine grained control and visibility into network
Assumes specialized hardware
  Limited Flow Table entries

## Slide 17: Dimensions of SDN Environments: Southbound Interface
OpenFlow
Flexible matching
  L2, L3, VLAN, MPLS
Flexible actions
  Encapsulation: IP-in-IP
  Address rewriting:
    IP address
    Mac address
BGP/XMPP/IS-IS/NetConf
Limited matching
  IS-IS: L3
  BGP+MPLS: L3+MPLS
Limited actions
  L3/l2 forwarding
  Encapsulation

## Slide 18: Dimensions of SDN Environments: Controller Types
Modular Controllers
Application code manipulates forwarding rules
  E.g. OpenDaylight, Floodlight
Written in imperative languages
  Java, C++, Python
Dominant controller style
High Level Controllers
Application code specifies declarative policies
  E.g. Frenetic, McNettle
Application code is verifiable
  Amendable to formal verification
Written in functional languages
  Nettle, OCamal

## Slide 19: BigSwitch
Controller Type
  Modular: Floodlight
Southbound API: OpenFlow
  OpenFlow 1.3
SDN Device: Whitebox
  (indigo)
SDN Flavor
  Underlay+Overlay

## Slide 20: Juniper Contrail
Controller Type
  Modular: OpenContrail
Southbound API: XMPP/NetConf
  BGP+MPLS
SDN Device: Vertical Stack
  Propriety Junos
SDN Flavor
  Overlay

## Slide 21: SDN EcoSystem
Arista
OF + proprietary
Underlay
Vertical Stack
Broadcom
OF + proprietary
Underlay
Vertical Stack
HP
OF
Underlay
Vertical Stack
Cisco
OF + proprietary
Underlay+Overlay
Vertical Stack
FloodLight
OF
Underlay+Overlay
Whitebox
Dell
OF
Underlay
Vertical Stack
HP
OF
Underlay
Vertical Stack
Alcatel
BGP
Overlay
Vertical Stack
Juniper
BGP+NetConf
Overlay
Vertical Stack

## Slide 22: SDN Stack
Southbound API: decouples the switch hardware from control function
  Data plane from control plane
Switch Operating System: exposes switch hardware primitives
Controller (Network O.S.)
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware

## Slide 23: Section2: Southbound API: OpenFlow

## Slide 24: OpenFlow
Developed in Stanford
  Standardized by Open Networking Foundation (ONF)
  Current Version 1.4
    Version implemented by switch vendors: 1.3
Allows control of underlay + overlay
  Overlay switches: OpenVSwitch/Indigo-light
PC

## Slide 25: How SDN Works: OpenFlow
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch H.W
Switch O.S
Switch H.W
Switch O.S
OpenFlow
OpenFlow

## Slide 26: OpenFlow: Anatomy of a Flow Table Entry
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
Match
Action
Counter
Forward packet to zero or more ports
Encapsulate and forward to controller
Send to normal processing pipeline
Modify Fields
When to delete the entry
VLAN
pcp
IP
ToS
Priority
Time-out
What order to process the rule
# of Packet/Bytes processed by the rule

## Slide 27: OpenFlow: Types of Messages
Asynchronous (Controller-to-Switch)
  Send-packet: to send packet out of a specific port on a switch
  Flow-mod: to add/delete/modify flows in the flow table
Asynchronous (initiated by the switch)
  Read-state: to collect statistics about flow table, ports and individual flows
  Features: sent by controller when a switch connects to find out the features supported by a switch
  Configuration: to set and query configuration parameters in the switch
Asynchronous (initiated by the switch)
  Packet-in: for all packets that do not have a matching rule, this event is sent to controller
  Flow-removed: whenever a flow rule expires, the controller is sent a flow-removed message
  Port-status: whenever a port configuration or state changes, a message is sent to controller
  Error: error messages
Symmetric (can be sent in either direction without solicitation)
  Hello: at connection startup
  Echo: to indicate latency, bandwidth or liveliness of a controller-switch connection
  Vendor: for extensions (that can be included in later OpenFlow versions)

## Slide 28: Dimension of SDN Applications: Rule installation
Proactive Rules
Reactive Rules
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 29: Dimension of SDN Applications: Rule installation
Proactive Rules
Controller pre-installs flow table entries
  Zero flow setup time
Requires installation of rules for all possible traffic patterns
  Requires use of aggregate rules (Wildcards)
  Require foreknowledge of traffic patterns
  Waste flow table entries
Reactive Rules
First packet of each flow triggers rule insertion by the controller
  Each flow incurs flow setup time
  Controller is bottleneck
  Efficient use of flow tables

## Slide 30: Dimensions of SDN Applications: Granularity of Rules
Microflow
WildCards (aggregated rules)
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 31: Dimensions of SDN Applications: Granularity of Rules
Microflow
One flow table matches one flow
Uses CAM/hash-table
  10-20K per physical switch
Allows precisions
  Monitoring: gives counters for individual flows
  Access-Control: allow/deny individual flows
WildCards (aggregated rules)
One flow table entry matches a group of flow
Uses TCAM
  5000~4K per physical switch
Allows scale
  Minimizes overhead by grouping flows

## Slide 32: Dimensions of SDN Applications: Granularity of Rules
Distributed Controller
Centralized Controller
Controller (N. O.S.)
Applications
Applications
Applications
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Controller (N. O.S.)
Applications
Applications
Applications
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Controller (N. O.S.)
Applications
Applications
Applications
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 33: Google’ B4 Application
Rule installation
  Proactive
Rule Granularity
  Aggregate
Distributed
  Multiple instances

## Slide 34: OpenFlow: Message Formats
Controller encapsulates message into an object
  Accessor functions to different fields
  No need to worry about crafting network packets

## Slide 35: OpenFlow Actions (Partial list from OpenFlow 1.0 spec)
Output to switch port (Physical ports & virtual ports). Virtual ports include the following:
  ALL (all standard ports excluding the ingress port) - flood
  CONTROLLER (encapsulate and send the packet to controller) – PACKET_IN message
  LOCAL (switch’s stack) – go through the IP layer, etc (mostly used for vSwitches)
  NORMAL (process the packet using traditional non-OpenFlow pipeline of the switch) – traditional L2 forwarding, L3 routing
Drop
Set fields (packet modification/header rewriting)
  Ethernet Source address
  Ethernet Dest address
  IP source & dest addresses, IP ToS, IP ECN, IP TTL, VLAN
  TCP/UDP source and destination ports
Strip (pop) the outer VLAN tag
Set queue ID when outputting to a port (Enqueue)
New in OpenFlow 1.1+
  Support for matching across mulitple tables
  Support for tunneling
  Support for Push/Pop mulitple VLAN/MPLS/PBB tags

## Slide 36: Section 2: SDN Use Cases

## Slide 37: SDN Use Cases
Network Virtualization (VMWare, Azure)
Port tapping (Big Switch’s BigTap)
Access control (Big Switch’s SNAC)
WAN Traffic Engineering (Google B4)
DDoS Detection (Defense4All)
Network Orchestration (OpenStack, VMWare)

## Slide 38: SDN Use Cases
WAN-Traffic engineering
  Google’s B4 (SIGCOMM 2013)
  Microsoft’s SWAN (SIGCOMM 2013)
Network Function Virtualization: Service Chaining
  SIMPLIFY/FlowTags (SIGCOMM 2013, NSDI 2014)
  Slick (ONS 2013)
Network virtualization
  Nicira, Azure, Google,
  VL2 & Portland (SIGCOMM 2009)
  CloudNaaS (SoCC 2011)
Seamless workload (VM) mobility
  (CrossRoads (NOMS 2012))
Data Center Traffic engineering
  Routing elephant flows differently (Hedera – NSDI 2010)
  Routing predictable traffic (MicroTE – CoNext 2011)
Port-Mirroring
  BigTap
  OpenSafe (INM/WREN 2011)

## Slide 39: SDN Use Case: Network Function Virtualization

## Slide 40
Network Policy:
Goals:
Detect attacks
Prevent unauthorized access
Firewall
IDS
Web
WEB
Firewall
IDS
Problem:
Traffic takes shortest path
Avoids middleboxes
  Servers are unprotected

## Slide 41
Network Policy:
Firewall
IDS
Web
WEB
Firewall
IDS
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 42
Network Policy:
Firewall
IDS
Web
WEB
Firewall
IDS
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 43
ONF NVF RoadMap

## Slide 44: Section 2: SDN Challenges

## Slide 45: Controller Availability
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 46: Controller Availability
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 47: Controller Availability
“control a large force like a small force: divide and conquer”
--Sun Tzu, Art of war
How many controllers?
How do you assign switches to controllers?
More importantly: which assignment reduces processing time
How to ensure consistency between controllers
Controller (N. O.S.)
Applications
Applications
Applications
Controller (N. O.S.)
Applications
Applications
Applications
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 48: SDN Reliability/Fault Tolerance
Controller (N. O.S.)
Applications
Applications
Applications
Controller: Single point of control
Bug in controller takes the whole network down
Existing network survives failures or bugs in code for any one devices

## Slide 49: SDN Reliability/Fault Tolerance
Controller (N. O.S.)
Applications
Applications
Applications
Controller: Single point of control
Bug in controller takes the whole network down
Single point of failure
Existing network survives failures or bugs in code for any one devices

## Slide 50: SDN Security
Controller (N. O.S.)
Applications
Applications
Applications
Controller: Single point of control
Compromise controller
If one device in the current networks are compromised the network may still be safe

## Slide 51: SDN Security
Controller (N. O.S.)
Applications
Applications
Applications
Controller: Single point of control
Compromise controller
Denial of Service attack the control channel

## Slide 52: Data-Plane Limitations
Limited Number of TCAM entries
  Currently only 1K
    Networks have more than 1K flows
  How to fit network in limited entries?
Limited control channel capacity
  All switches use same controller interface
  Need to rate limit control messages
    Prioritize certain messages
Limited switch CPU
  Less power than a smartphone 
  Limit control messages and actions that use CPU
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 53: Debugging SDNs
Problems can occur anywhere in the SDN stack
  How do you diagnose each type of problem?
Network O.S.
Applications
Applications
Applications
Switch Operating System
Switch Hardware
Buggy
App
Buggy
NOS
Switch Operating System
Switch Hardware
Buggy
Switch
H/W
Buggy
Switch

## Slide 54: Section 2: SDN – A Systems Approach to SDN

## Slide 55: Conclusion
An overview of SDN technologies
Introduction to OpenFlow
Developing Applications on OpenFlow