## Slide 1: SDN Abstractions

## Slide 2: In an SDN Ideal World, we want…
multiple applications (Composition):
  So, need to worry about sharing.
  About isolation.
Network policies affect multiple devices
  Need to worry about consistency of updates
We don’t want any bugs
  We need to verify App and controllers
Scalable control plane
  Make sure data is distributed

## Slide 3: So.. We have several problems
Composition: Network Sharing
  PANE, HFT, Pyretic
Composition/isolation: Network Isolation
  Pyretic, Nicira
Consistent Updates
  Pyretic, Zupdates, ConsistentUpdates
Verification
  Vericon [PLDI’14], Veriflow, Libra
Scalable/Distributed control place
  Onix [OSDI 10], Kandoo [HotSDN 11], Beehive [HotNets 14], ElasticCon [ ANCS ‘14]

## Slide 4: Are these Problems New?
No…..
  We’ve always wanted verification
  We’ve always wanted consistent updates
  Always wanted isolation
We never really worried about
  Network sharing: everything was made by Cisco and cisco figured out sharing. Or we manually figured it out: e.g QoS
  Scalable control plane: all decentralized.

## Slide 5: SDN … and logical centralization
As indicated in veriflow
  A central location … we can debug from
Programmatic API
  We can more directly control the network
  We can make more guarantees
    Consistency becomes a huge problem when you start making security/performance guarantees

## Slide 6: Network Sharing: PANE/HFT
Operators and users depend on the network but find ways to work around the network.
They employ overlays to find better paths
They use pings to measure bandwidth and manually shift traffic.

## Slide 7: Participatory Networking
Rather than working around the network, application should work with the network to achieve their goals
Apps need to:
  Learn from the network: available resources
  Write to the network: make requests for current/future resources. E.g. bandwidth, links …
Notes: To do this applications need to be able to learn from the network what resources are available and then be able to request resources from the network or inform the network of future requests. The applications should be able to inform the network of their requirements and thus to be able to request resources from the network.

## Slide 8: So a share: Skype example
I’m skype application, I would like to request 20MB bandwidth for all port 432 traffic.
  Share:
    App/User: skype
    Message type: request (20MB)
    Flow-Group: traffic on port 432
Notes: a share gives a set of Apps/Users some privileges to affect a set of flows in the network
Shares: PANEs realization of a capability. Its a token that encapsulates authority to use a resource:
Flowgroup: some subset of the network’s flow
Principals: ower of the share. can delegate to another user. or make a subshare for someone else
privileges:what actions can be performed on a share

## Slide 9: So a share: Security example
I’m firewall application, I would like to request all port 80 traffic to go to a Middleboxes .
  Share:
    App/User: firewall
    Message type: send traffic to a middlebox ‘way-point’
    Flow-Group: traffic on port 80
Notes: a share gives a set of Apps/Users some privileges to affect a set of flows in the network
Shares: PANEs realization of a capability. Its a token that encapsulates authority to use a resource:
Flowgroup: some subset of the network’s flow
Principals: ower of the share. can delegate to another user. or make a subshare for someone else
privileges:what actions can be performed on a share

## Slide 10: So a share: performance example
I’m windows update application, I would like to see how much B/W is available.
  Share:
    App/User: window-update
    Message type: query for available BW
    Flow-Group: N/A
Notes: a share gives a set of Apps/Users some privileges to affect a set of flows in the network
Shares: PANEs realization of a capability. Its a token that encapsulates authority to use a resource:
Flowgroup: some subset of the network’s flow
Principals: ower of the share. can delegate to another user. or make a subshare for someone else
privileges:what actions can be performed on a share

## Slide 11: PANE Controller
allows for resource sharing by allowing people to specify `shares`
A Share, includes
  App/User allowed to make requests
  Types of messages that can be sent to the network
  What IP/Subnets can the requests affect
Notes: a share gives a set of Apps/Users some privileges to affect a set of flows in the network
Shares: PANEs realization of a capability. Its a token that encapsulates authority to use a resource:
Flowgroup: some subset of the network’s flow
Principals: ower of the share. can delegate to another user. or make a subshare for someone else
privileges:what actions can be performed on a share

## Slide 12: Types of Messages/Requests
actions: rate-limit, bandwidth requests, path control(way-points/avoidances), access-control
Queries: Network weather service: (aggregate TM), Link info: anything OF exposes
Hints: Hints: e.g. size of flow, priority, deadline, predictability of TM

## Slide 13: PANE: Challenges.
Isolation between different tenants.
Enforcement resource limitations.
Safely provide control/visibility over the network.
detect and resolve resource conflicts.
Notes: There are two challenges from arise from this (Classic resource sharing challenges):
Isolation between different tenants. Ensuring that one application doesn’t adversely affect another.
Enforcement resource limitations. No can use more than the set of resources appropriated to them.
Safely provide control/visibility over the network.
detect and resolve resource conflicts.

## Slide 14: Share Tree/HFT
Build a hierarchical structure that shows how the flowgroups that a share acts on are related.
Notes: PANE builds a share tree from all shares, which shows how shares are related.
Each sub-share is a subset in terms of flow group
The sub-share’s actions can not be more permissive/powerful than the parent-share.

## Slide 15: How does PANE Work: User submits actions
User/App submits a request with
  The share the user owns.
  The action to perform
  The Flowgroup to perform action on.

## Slide 16: How does PANE Work: verifies authentication + resource availability
PANE verifies
  Ability to perform action on flow-group based on ‘shares’
  Convert request into a policy
  Can make a policy tree.
PANE checks to see if enough resources exist:
  Conflict Resolution!!!
  Two apps can have shares that give 20MB
  But network only has 30MB so….

## Slide 17: Life of a Request in PANE

## Slide 18: Contributions:
Delegation of privileges (capabilities).
  Provide fine-grained control over resources.
  Can further chop-up and delegate resources to others.
Hierarchical conflict resolution
  Detect and resolve conflicts

## Slide 19: Interesting Tid-Bits about PANE
Single admin domain.
During failures: accepted requests may be rejected due to resource limitations.