## Slide 1: Logically Centralized Control
Class 2

## Slide 2: Types of Networks
ISP Networks
  Entity only owns the switches
  Throughput: 100GB-10TB
  Heterogeneous devices: laptop/desktop
  Medium latency: 20-80 milliseconds
Enterprise Networks
  One entity owns many of the servers + switches
  Throughput: 10G-40GB
  Heterogeneous devices: laptop/desktop
  Medium latency: 5-10 milliseconds
Clouds/Data Centers
  One entity owns servers + switches
  Extra low latency between 2 devices (20 microseconds)
  Homogenous devices

## Slide 3: Network Review
Edge Device
  Connects hosts
  Sees little traffic (GB)
  Sees a small number of flows
Implications:
  Can do per flow processing.
  Can store per for state
Core
  Connects other switches
  Lots of traffic (TB)
  VERY Expensive
  See a lot of flows
Implications
  Can’t do per flow processing!
  Can’t store per flow state

## Slide 4: Router Review
Fast path/data path
  Specialized H/W
    Very Expensive
    Takes 3-5 years to change
  Performs processing on every packet
    Very very fast
Slow Path/control plane
  Has general purpose CPU
  Runs routing algorithms
  Only works on a few packets
    Very very slow
    Very very slow
  Can’t process all packets

## Slide 5: Inside a Single Network
Data Plane
Distributed routers
Forwarding, filtering, queueing
Based on FIB or labels
Management Plane
Figure out what is happening in network
Decide how to change it
Shell scripts
Traffic Eng
Databases
Planning tools
OSPF
SNMP
netflow
modems
Configs
OSPF
BGP
Link metrics
OSPF
BGP
OSPF
BGP
Control Plane
Multiple routing processes on each router
Each router with different configuration program
Huge number of control knobs: metrics, ACLs, policy
FIB
FIB
FIB
Routing policies
Packet filters

## Slide 6: Time Scales
 | Data | Control | Management
Time scales | Packets | Events | Humans
Task | Forwarding/buffering/filtering/scheduling | Routing, circuit set-up | Analysis, configuration
Location | Hardware Specialized hardware Processes at line rate. Every packet Very fast | Router software Uses CPU Can only process a small number of packets Very slow | Human or perl scripts

## Slide 7: Ideally…
Split load between S5 and S6
Shut down S6 for maintenance on May 1
forwarding state
Managing network in a simple way
Directly and explicitly apply policies to network
accurate network view
S1
S2
S3
S4
S5
S6
Internet
Notes: To motivate our work, let’s think about how we really want to manage a network and look at what the reality is.
This is what we call direct control paradigm, where control policies are made explicit and they are directly applied to network.
Are we there yet?

## Slide 8: Indirect Control - Fact #1: Infer network view by reverse engineering
Probe routers to fetch configuration
Monitor control traffic (e.g., LSAs, BGP update)
probe routers and guess network view
S1
S2
S3
S4
S5
S6
Internet
?
?
?
?
?
Notes: To motivate our work, let’s think about how we really want to manage a network and what the reality is.

## Slide 9: Indirect Control - Fact #2: Policies buried in box-centric configuration
Change OSPF link weights on S2, S3, S4..
Modify routing policies on S2, S3, S4…
configuration commands
Many knobs to tune
Trial and error
probe routers and guess network view
S1
S2
S3
S4
S5
S6
Internet
?
?
?
?
?
Notes: To motivate our work, let’s think about how we really want to manage a network and what the reality is.

## Slide 10: Complex configuration is error-prone and is causing network outages
interface Ethernet0
ip address 6.2.5.14 255.255.255.128
interface Serial1/0.5 point-to-point
ip address 6.2.2.85 255.255.255.252
ip access-group 143 in
frame-relay interface-dlci 28
router ospf 64
redistribute connected subnets
redistribute bgp 64780 metric 1 subnets
network 66.251.75.128 0.0.0.127 area 0
router bgp 64780
redistribute ospf 64 match route-map 8aTzlvBrbaW
neighbor 66.253.160.68 remote-as 12762
neighbor 66.253.160.68 distribute-list 4 in
access-list 143 deny 1.1.0.0/16
access-list 143 permit any
route-map 8aTzlvBrbaW deny 10
match ip address 4
route-map 8aTzlvBrbaW permit 20
match ip address 7
ip route 10.2.2.1/16 10.2.1.7

## Slide 11: Indirect Control - Fact #3: Indirect Control Creates Subtle Dependencies
Example:
  Policy #1: use C as egress point for traffic from AS X
  Policy #2: enable ECMP for A-C flow
AS Y
1
1
2
3
3
1
AS X
1
4
Desired
Unexpected!
C
B
A
D

## Slide 12: Indirect Control leads to …
  62% of network downtime in multi-vendor networks comes from human-error
  80% of IT budgets is spent on maintenance and operations .

## Slide 13: An Architecture Question to Study
How should the functionality that controls a network be divided up?
Important: everyone hates net outages
Practical: solutions can be implemented without changing IP or end-hosts
Relevant: trends toward separating decision-making from forwarding
Unsolved: problem is not solved by running BGP/OSPF on faster servers

## Slide 14: Our Proposal: Dissemination and Decision Planes
What functions require a view of entire network and network objectives?
Path selection and traffic engineering
Reachability control and VPNs
! Decision plane
What functions must be on every router to support creation of a network-wide view?
Topology discovery
Report measurements, status, resources
Install state (e.g., FIBs, ACLs) into data-plane
! Dissemination plane

## Slide 15: Direct Control: A New World
Express goals explicitly
  Security policies, QoS, egress point selection
  Do not bury goals in box-specific configuration
  Make policy dependencies explicit
Design network to provide timely and accurate view
  Topology, traffic, resource limitations
  Give decision maker the inputs it needs
Decision maker computes and pushes desired network state
  FIB entries, packet filters, queuing parameters
  Simplify router functionality
  Add new functions without modifying/creating protocols or upgrading routers

## Slide 16: How can we get there?
D
Routing Table
Access Control Table
NAT Table
Tunnel Table
Decision Computation Service
Generating table entries
Data Plane
Modeled as a set of tables
Install table entries
Discovery
Dissemination Service
D
D
D
4D

## Slide 17: Discuss Implementations Possibilities
Decision Plane
  Centralized, or
  Distributed
Dissemination Plane
  In-band, or
  Out-of-band
Data Plane
  Flow table entries
  Piece of code run at every router
  Piece of code in each packet
Notes: Choice based on reliability requirements
Data plane evolution should be driven by needs of decision and dissemination planes