## Slide 1: Class 3: SDN Stack
Theophilus Benson

## Slide 2: Outline
Background
  Routing in ISP
  Cloud Computing
SDN application stack revisited
Evolution of SDN
  The end of device Equality

## Slide 3: Routing In ISP
Within ISP (IGP): go from ingress to egress
Across ISP (EGP/BGP): figure out which egress
Which endpoint
Which endpoint
Which endpoint
What is next hop
Notes: Intradomain routing: domains must carry packets from the ingress peering domain to the egress peering domain

## Slide 4: Routing In ISP
Within ISP (IGP): go from ingress to egress
Across ISP (EGP/BGP): figure out which egress
What is set of ISP
What is set of ISP
What is set of ISP
What is set of ISP
Notes: Interdomain: carry the packet from domain A to domain B

## Slide 5: Routing In ISP:OSPF
Distribute reachability inform
Work on IP-addresses
10.10.0/24
10.11.0/24
54.23.4/24
54.23.4/24
10.10.0/24
10.11.0/24
54.23.4/24
54.23.4/24
10.10.0/24
10.11.0/24
54.23.4/24
54.23.4/24

## Slide 6: OSPF Draw-Backs
Requires complex look: longest prefix match
Requires large tables
Slow to reach to failures
  2 minutes
10.10.0/24
10.11.0/24
54.23.4/24
54.23.4/24
10.10.0/24
10.11.0/24
54.23.4/24
54.23.4/24
10.10.0/24
10.11.0/24
54.23.4/24
54.23.4/24

## Slide 7: Enter-MPLS
Fast Re-Route (FRR)
  Manually setup Back-up paths (react in milliseconds)
Route on a smaller number of labels
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24
54.23.4.0/24
10.10.0.0/24
10.11.0.0/24
54.24.4.0/24
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24

## Slide 8: Enter-MPLS
Fast Re-Route (FRR)
  Manually setup Back-up paths (react in milliseconds)
  Route on a smaller number of labels
  Edge does great per-packet processing
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24
Red label
Blue label
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24
54.23.4.0/24
10.10.0.0/24
10.11.0.0/24
54.24.4.0/24

## Slide 9: Enter-MPLS
Distinguish core from edge
  Edge: uses IP and classifies packet to label
  Core: forwards based on packet
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24
Red label
Blue label
10.10.0/24
10.11.0/24
54.23.4/24
54.24.4/24
54.23.4.0/24
10.10.0.0/24
10.11.0.0/24
54.24.4.0/24

## Slide 10: Cloud Computing
Applies virtualization technology to a data center
ISP
Cloud
Data Center

## Slide 11: Cloud Computing
Applies virtualization technology to a data center
  Allows you to run VMs for different costumers
  Share the physical resource
ISP
Cloud
Data Center
Provides illusion of:
  Unlimited resources
  Need more CPU/memory?
    Just get more VMS!!!

## Slide 12: Cloud Computing
ISP
Cloud
Data Center
Physical Servers
Virtual Switch
Virtual machines
(Virtual Servers)
Physical Switches
Traditional Data Center. All Hardware.
Virtual infrastructure, all software.
Notes: Virtualization (VMs) is supported by hypervisors
Hypervisors use software switch to connect VMs
Make this software switch SDN-compatible
  And you’ll be able to deploy SDN without any new HW
Open vSwitch is now in Linux, Xen, and coming soon to other Oses and hypervisors

## Slide 13: SDN: The OpenFlow Flavor
A network is …
Network O.S.
Applications
Applications
Applications
Switch Operating System
Switch Hardware
Switch Operating System
Switch Hardware
Switch Operating System
Switch Hardware
Switch Operating System
Switch Hardware

## Slide 14: SDN: The OpenFlow Flavor
A network supports …
  Innovation in App
  Innovation in N/W O/S
Requires all devices to be the same.
  But you don’t need same functionality everywhere
    Forwarding V. Encryption V.
  You don’t need all devices to handle the same type of traffic
    Cellular V. Core V. IPTV
Forcing device homogeneity
  Limits ability to move forward
Hard to balance between
Generality and practicality
Limits evolvabilty by forcing all to evolve at same speed.
Flexible API allows
Notes: Generality – match on all bits
Pracitality – match on subset of bits

## Slide 15: Background
Network infrastructure design is guided by network requirements and network interfaces
Network requirements come from two sources:
  Host : want their packets to travel to a particular destination
  (ii) Network operator : traffic engineering, virtualization, tunneling and isolation

## Slide 16: Different Interfaces
There are three relevant interfaces
  Host -Network : inform the network of host’s requirements. E,g. destination and QoS
  Operator-Network : inform the network of operator’s requirements. E.g. configuration of network rules.
  Packet-Switch : identify packet to a switch
Notes: H-N: Where to go! What quality I want.
O-N: how to treat different destinations. How to treat different quality of services classes.
P-S: which rule

## Slide 17: Evolution of Data Center Networks…
Everyone is
Equal
OpenFlow
MPLS
Fabric
Host-Network
Operator-Network
Packet-Switch
IP-addresses
MPLS label
Bad config interface
OpenFlow API
Notes: three problems
  no simplified hardware
  no sufficient flexibility
  it unnecessarily couples the host requirements to the network core behavior

## Slide 18: Application of Fabric To Reality: The Cloud
Data Center
Physical Servers
Virtual Switch
Virtual machines
(Virtual Servers)
Physical Switches

## Slide 19: Application of Fabric To Reality: The Cloud
Data Center
Physical Servers
OpenVirtual Switch
Virtual machines
(Virtual Servers)
Abstract Away this Layer
One Big Switch abstraction.
Forwards based on server IP
Server IP is the Label here.
Performs Classification:
VM address-> server address
Edge  core (Think: IP  MPLS)
Can implement:
QoS
Migration
monitoring
Access Control
Notes: Make this software switch SDN-compatible
  And you’ll be able to deploy SDN without any new HW
Open vSwitch is now in Linux, Xen, and coming soon to other Oses and hypervisors
Vswitches are enough to implement most functions
  Access control, QoS, mobility, migration, monitoring,…
Physical network becomes static crossbar
  Simple to implement and manage
  Components can be legacy and static

## Slide 20: Application of Fabric To Reality: The Cloud
Data Center
Physical Servers
OpenVirtual Switch
Virtual machines
(Virtual Servers)
Abstract Away this Layer
One Big Switch abstraction.
Forwards based on server IP
Server IP is the Label here.
Performs Classification:
VM address-> server address
Edge  core (Think: IP  MPLS)
Can implement:
QoS
Migration
monitoring
Access Control
The VM can evolve independently of the physical infrastructure.
VMs can go to IPv6 while physical stays IPv4.
VMs can had advance functionality added by modifying virtual switch
Notes: Make this software switch SDN-compatible
  And you’ll be able to deploy SDN without any new HW
Open vSwitch is now in Linux, Xen, and coming soon to other Oses and hypervisors
Vswitches are enough to implement most functions
  Access control, QoS, mobility, migration, monitoring,…
Physical network becomes static crossbar
  Simple to implement and manage
  Components can be legacy and static

## Slide 21: Application of Fabric To Reality: The ISP

## Slide 22: Application of Fabric To Reality: The ISP
Replace Edge switches with servers
  Get extreme flexibility. Easy to change code
  Bad scaling. Need multiple servers
Notes: Domains can be build like “fabrics”
Edge uses software forwarding
  Controlled by edge controller

## Slide 23: Application of Fabric To Reality: The ISP
Core: uses hardware label-based forwarding
Edge: does classification
  Can do other complex processing: encryption, QoS
Notes: Core uses hardware label-based forwarding
Only edge understands interdomain delivery
  Change in “architecture” (e.g., IPv4 to IPv6) only requires change to edge controller software
  Software-defined Internet Architecture

## Slide 24: Routing In ISP
Within ISP (IGP): go from ingress to egress
Across ISP (EGP/BGP): figure out which egress
What is set of ISP (BGP)
What is set of ISP(BGP)
What is set of ISP (BGP)
What is set of ISP (BGP)
alice
bob
EGP for distributing reachability information
Notes: Interdomain: carry the packet from domain A to domain B

## Slide 25: Routing In ISP
Running SDN in each ISP
  Edge controller runs BGP
What is set of ISP (BGP)
What is set of ISP(BGP)
alice
bob
What is set of ISP(BGP)
EGP for distributing reachability information
Notes: changing how domains are addressed again only requires a change to the controller software. Because the edge routers use software forwarding.
Switches from BGP to something else.

## Slide 26: Routing In ISP
Hybrid approach of BGP+SDN
  Edge controller negotiates with border routers
What is set of ISP(BGP)
alice
bob
What is set of ISP (BGP)
What is set of ISP (BGP)
What is set of ISP (BGP)
EGP for distributing reachability information
Notes: changing how domains are addressed again only requires a change to the controller software. Because the edge routers use software forwarding.
Switches from BGP to something else.

## Slide 27: Routing In ISP
Replace the BGP with a Content Centric approach.
What is closest cache
What is closest cache
alice
bob
What is closest cache
Notes: changing how domains are addressed again only requires a change to the controller software. Because the edge routers use software forwarding.
Switches from BGP to something else.

## Slide 28: Discussion