## Slide 1: Measurement in Networks & SDN Applications

## Slide 2: Interesting Questions
Who is sending a lot to a subnet?
  Heavy Hitters
Is someone doing a port Scan?
Is someone getting DDoS-ed?
Who is getting traffic for a naughty website?
How many people have downloaded from a naughty site?
Which links have the most bytes

## Slide 3: Port Scan
Try to find vulnerability in a host
  Idea scan all the ports on the host to see which are open
    A scan: a small hello packet to see if host responds
  After finding the open port you can perform other attacks

## Slide 4: DDoS
Try to attack a host/server
  Make sure the server can’t respond to anyone else
  Send it a bunch of traffic until out of memory
  Send it a bunch of traffic until no more bandwidth
DoS: attack the server from one machine
DDoS: attack the server from many machines
  Harder to defend against.

## Slide 5: How do we measure things?
Switches count bytes/packets
  NetFlow/sFlow: # bytes/packets per flow
    To scale: samples packets and performs calculations based on samples.
      1 in ever n packets
    Implications: don’t see all packets.
  SNMP: # bytes/packets per link

## Slide 6: Interesting Questions
Who is sending a lot to a subnet?
Is someone doing a port Scan?
Is someone getting DDoS-ed?
Who is getting traffic for a naughty website?
How many people have downloaded from a naughty site?
Which links have the most bytes?
Netflow
SNMP

## Slide 7: Why can’t questions be answered?
When you sample  you miss packets.
  Increasing the sampling rate leads to huge resource overheads.
So can’t answer questions:
  You miss the packets when you check sampling
  Is someone doing a port Scan?
    Is there a short lived connection from one server to many ports on another server?
  Is someone doing a DDoS?
    Is there a short lived connection from many servers to one?

## Slide 8: Solution…….
  You don’t want to sample because you miss stuff
  But you can’t always process everything because it is hard to scale
Use online streaming algorithms
  See OpenSketch for more…

## Slide 9: What are SDN Applications?

## Slide 10: How we use the network
Ensuring reachability: routing/forwarding traffic
  Bad things: loop-holes, blackholes

## Slide 11: How do we use the network
Network Address Translation
  You have a small number of IP address; e.g. 1
  But you want to have many devices; tablet/phone
    Each one needs it own IP address
    So you share them
External IP
123.12.392.3
Internal IP
10.10.0.1
Internal IP
10.10.0.2
Port | Internal IP
23 | 10.10.0.1
34 | 10.10.0.2

## Slide 12: How do we use the network
Load balancing: make sure servers get equal number of requests

## Slide 13: How do we use the network
Load balancing: make sure servers get equal number of requests

## Slide 14
L.B.
Security
NAT
Physical View
Device State
Policy
Veriflow|H.A.S.|Libra
Network OS
Invariant has been violated!
There’s a bug. What Next?
Hub

## Slide 15: How are Networks managed

## Slide 16: How are Networks managed
In a hierarchical manner
  With control delegated from top to bottom
  Resource delegated in a similar manner

## Slide 17: How can SDN support such delegation?
Hierarchical capabilities.
See more in the PANE paper.