## Slide 1: OpenSketch
Slides courtesy of Minlan Yu

## Slide 2: Management = Measurement + Control
Trafﬁc engineering
  Identify large traffic aggregates, traffic changes
  Understand flow characteristics (flow size, delay, etc.)
Performance diagnosis
  Why my application has high delay,
  low throughput?
Accounting
  Count resource usage for tenants
Notes: Management is important, yet underexplored
  Taking 80% of IT budget
  Responsible for 62% of outages
  Measurement is at least half of network management
  Figuring out what’s going on is harder than
  deciding what to do

## Slide 3: Measurement is Increasingly Important
Increasing network utilization in larger networks
  Hundreds of thousands of servers and switches
  Up to 100Gbps in data centers
  Google drives WAN links to 100% utilization
Requires better measurement support
  Collect fine-grained flow information
  Timely report of traffic changes
  Automatic performance diagnosis
Notes: for me it was hard to relate the conclusion (italic text) to the heading of each bullet (It uses audience brain!)

## Slide 4: Yet, measurement is underexplored
Vendors view measurement as a secondary citizen
  Control functions are optimized w/ many resources
  NetFlow/sFlow are too coarse-grained
Operators rely on postmoterm analysis
  No control on what (not) to measure
  Infer missing information from massive data
Network-wide view of traffic is especially difficult
  Data are collected at different times/places
Notes: SLOW down, spend more time on this

## Slide 5: Software-defined Measurement
SDN offers unique opportunities for measurement
  Vendors build simple, reusable primitives
  Operators decide what to measure dynamically
  Operators regain network-wide view
Controller
Heavy Hitter detection
Configure resources
1
Fetch statistics
2
(Re)Configure resources
1
Change detection

## Slide 6: Challenges
Diverse measurement tasks
  Generic measurement primitives at switches
  Modularized measurement library in the controller
Limited switch resources for measurement
  New data structures to reduce memory usage
  Multiplexing across many measurement tasks

## Slide 7: Rethink Measurement Abstraction for SDN
API to the data plane (OpenFlow)
Fields action counters
Src=1.2.3.4drop, #packets, #bytes
Switches
Forward/measure packets
Controller
Configure devices and
collect measurements
Notes: Packet/Byte counters are not enough
  Large traffic aggregates: too many counters at switches (one counter for each micro flow)
  Pull too many statistics to the controller

## Slide 8: Tradeoff of Generality and Efficiency
Generality
  Supporting a wide variety of measurement tasks
  Who’s sending a lot to 23.43.0.0/16?
  Is someone being DDoS-ed?
  How many people downloaded ﬁles from 10.0.2.1?
Efficiency
  Enabling high link speed (40 Gbps or larger)
  Ensuring low cost (Cheap switches with small memory)
  Easy to implement with commodity switch components
Notes:   E.g., Cisco NetFlow

## Slide 9: NetFlow: General, Not Efficient
General
  Log sampled packets, or flow-level counters
  OK for many measurement tasks
Not efficient for any single task
  It’s hard to determine the right sampling rate
  Measurement accuracy depends on traffic distribution
  Turned off or not even available in datacenters
Notes:   Accuracy depends on traffic distribution
  Different sampling solutions for different problems

## Slide 10: Streaming Algo: Efficient, Not General
Efficient for individual task
  E.g. Who’s sending a lot to host A?
  Count-Min Sketch:
Not general
  Require customized hardware or network processors
  Hard to implement all solutions in one device
# bytes from 23.43.12.1
3
0
5
1
9
0
1
9
3
0
1
2
0
3
4
Hash2
Hash1
Hash3
Data plane
Query: 23.43.12.1
5
3
4
Pick min: 3
Control plane
Notes:     Bitmap for #unique items, Bloom filter for set member check
  Summarize packet information with Sketches

## Slide 11: Today Sketches are Developed to Improve Precision
Pro’s
  Sketches are optimized algorithms
  Use minimal space
  Very accurate
Con’s
  Each Sketch require unique specialized hardware
  Sketches do not generalize
Goal:
  General infrastructure that supports multiple sketches

## Slide 12: Where is the Sweet Spot?
Efficient
General
NetFlow/sFlow
(too expensive)
Streaming Algo
(Not practical)
OpenSketch
General, and efficient data plane based on sketches
Modularized control plane with automatic configuration
Notes: A new data structure that harnesses the capacity of the TCAMs across all the switches to give the illusion of a much larger TCAM.

## Slide 13: Flexible Measurement Data Plane
Picking the packets to measure
  Classify flows with different resources/accuracy
    Filter out traffic for 23.43.0.0/16
  Hashes to represent a compact set of flows
    Bloom filter for a set of blacklisting IPs
Storing and exporting the data
  Diverse mappings between counters and flows
  E.g., More accuracy for elephant flows
  E.g., Volume counter vs distinct counters
Notes:   A table with flexible indexing
  Complex indexing using hashes and classification

## Slide 14: Insights
Measurement task can be viewed as SQL-ish queries
  Select count(*) from * where ip= <blah> group by <bah>
    Traffic-count: Select count(*) from * where dstip=10.10.20.3 group by SrcIP
    Select count(*) from * group by packet-content
  The group by: can be accomplished by a hash
  The where: can be accomplished by a classifier
  The count: by a count primitive

## Slide 15: A three-stage pipeline
# bytes from 23.43.12.1
3
0
5
1
9
0
1
9
3
0
1
2
0
3
4
Hash2
Hash1
Hash3
Notes: Classification is missing, match on other packet header fields, hash values.

## Slide 16: Build on Existing Switch Components
A few simple hash functions
  4-8 three-wise or five-wise independent hash functions
  Leverage traffic diversity to approx. truly random func.
A few TCAM entries for classification
  Match on both packets and hash values
  Avoid matching on individual micro-flow entries
Flexible counters in SRAM
  Logical tables with flexible indexing
  Access counters by addresses
Notes: Different

## Slide 17: Modularized Measurement Libarary
A measurement library of sketches
  Bitmap, Bloom filter, Count-Min Sketch, etc.
  Easy to implement with the data plane pipeline
  Support diverse measurement tasks
Implement Heavy Hitters with OpenSketch
  Who’s sending a lot to 23.43.0.0/16?
  count-min sketch to count volume of ﬂows
  reversible sketch to identify ﬂows with heavy counts in the count-min sketch

## Slide 18: Support Many Measurement Tasks
Measurement Programs | Building blocks | Line of Code
Heavy hitters | Count-min sketch; Reversible sketch | Config:10 Query: 20
Superspreaders | Count-min sketch; Bitmap; Reversible sketch | Config:10 Query:: 14
Traffic change detection | Count-min sketch; Reversible sketch | Config:10 Query: 30
Trafﬁc entropy on port ﬁeld | Multi-resolution classiﬁer; Count-min sketch | Config:10 Query: 60
Flow size distribution | multi-resolution classiﬁer; hash table | Conﬁg:10 Query: 109

## Slide 19: Resource management
Automatic configuration within a task
  Pick the right sketches for measurement tasks
  Based on provable resource-accuracy curves
Resource allocation across tasks
  Operators simply specify relative importance of tasks
  Minimize weighted error using convex optimization
  Decompose to the optimization of individual tasks
Notes:   Allocating resources across sketches

## Slide 20: OpenSketch Architecture

## Slide 21: OpenSketch Conclusion
OpenSketch:
  Bridging the gap between theory and practice
Leveraging good properties of sketches
  Provable accuracy-memory tradeoff
Making sketches easy to implement and use
  Generic support for different measurement tasks
  Easy to implement with commodity switch hardware
  Modularized library for easy programming