## Slide 1: Dream
Slides Courtesy of Minlan Yu (USC)

## Slide 2: Challenges in Flow-based Measurement
Controller
Configure resources
1
Fetch statistics
2
(Re)Configure resources
1
Heavy Hitter detection
Heavy Hitter detection
Heavy Hitter detection
H
Change detection
Dynamic Resource Allocator
Many Management tasks
Limited resources (<4K TCAM)
Notes: Many measurement tasks
  Task types: Heavy hitter, Change detection
  Header fields: Source IP, Destination port
  Traffic aggregate: To drill down
  Per-tenant tasks
Limited measurement resources
  Limited CPU for measurement
  Cheap switches with limited memory
    We focus on hardware switches with TCAM

## Slide 3: Last Class: OpenSketch
Use sketch to perform measurements
Sketches are very efficient (space wise)
Requites a combination of TCAM and SRAM
  Requires the same flow to go through multiple stages
Sketches have 3 phases.
  Many OpenFlow 1.0 switches don’t support multi-stage matching
  OpenFlow 1.3> supports some multi-stage matching

## Slide 4: Flow-based Measurement
26
-
-
5
2
3
26
13
13
5
2
3
Divide
Merge
31
31
Flow-based counters
  Match on multiple packet header fields
  Report #bytes/#packets
  Heavy hitters, change detection, etc.
Monitor nodes in IP prefix tree
  E.g., Identify source IPs over 10
  Divide to increase accuracy
  Merge to save TCAM entries
Notes:   Cause of error: Monitor ancestors of large leaves

## Slide 5: Recall
To make accuracy gurantees
  You need to know traffic matrix
  You need to know for given algorithm what is the space to accuracy trade-off

## Slide 6: Diminishing return of resources
Tradeoff accuracy for more resources
  More resources make smaller accuracy gains
  Operators can accept an accuracy bound <100%
Recall=
detected true HH/all
Challenge: No ground truth of resource-accuracy
Notes: Finding 8Mbps heavy hitters on CAIDA trace
This curve is the same for different traffic, different measurement tasks, and has been observed papers
  More resources find less significant outputs

## Slide 7: Spatial/Temporal Resource Multiplexing
Temporal multiplexing across tasks
  Traffic varies over time, and accuracy depends on traffic
Spatial multiplexing across switches
  A task needs different resources across switches
Recall=
detected true HH/all
Switch 1
Switch 2
2
1
2
1
Challenge: Handle traffic and task dynamics across switches
Notes: Accuracy changes with traffic and traffic changes overtime
To reach an accuracy, we need to dynamically change its resources
Switch 1 needs more resources

## Slide 8: Multiplexing Resources Among Tasks
A task may need more resources
  At a specific time
  At a specific switch
But we can multiplex
Time=0
Time=1
Switch 1
Switch 2
Temporal multiplex
Spatial multiplex
2
1
2
1
2
1
2
1

## Slide 9: DREAM Framework
Controller
Configure resources
1
Fetch statistics
2
(Re)Configure resources
1
TCAM-based Measurement Framework
Dynamic Resource Allocator
Estimated accuracy
Allocated resource
Estimated accuracy
Allocated resource

## Slide 10: TCAM-based Measurement Framework
General support for different types of tasks
  Heavy hitters, Hierarchical HHs, change detection
Resource aware
  Maximize accuracy given limited resources
Network-wide
  Measuring traffic from multiple switches
  Assume each flow is seen at one switch (e.g., at sources)
Notes: Stress that each flow is at each source
  Multiple switches: e.g., HHs from different switches
    Assume: Each flow is seen at one switch (e.g., at sources)

## Slide 11: Challenges
No ground truth of resource-accuracy
  Hard to do traditional convex optimization
  We propose new ways to estimate accuracy on the fly
  Adaptively increase/decrease resources accordingly
Spatial & temporal changes
  Task and traffic dynamics across switches
  Temporal: Adjust resources based on traffic changes
  Spatial: Dynamically allocate resources across switches

## Slide 12: Divide & Merge at Multiple Switches
Divide: Monitor children to increase accuracy
  Requires more resources on a set of switches
    E.g., needs an additional entry on switch B
Merge: Monitor parent to free resources
  Each node keeps the switch set it frees after merge
  Finding the least important prefixes to merge is the minimum set cover problem
26
13
13
00*
01*
0**
{A,B}
{B,C}
{A,B,C}
5
2
3
10*
11*
1**
{B}
{B}
{B}
Notes: Change the example to original ones

## Slide 13: Task Implementation
Controller
Configure resources
1
Fetch statistics
2
(Re)Configure resources
1
Heavy Hitter detection
Heavy Hitter detection
Heavy Hitter detection
H
Change detection
Dynamic Resource Allocator
Estimated accuracy
Allocated resource
Estimated accuracy
Allocated resource

## Slide 14: Accuracy Estimation
Leverage all the monitored counters
  Precision: every detected HH is a true HH
  Recall:
    Estimate missing HHs using counter and level
76
26
50
13
13
4
9
12
1
15
35
20
15
0
15
000
001
010
011
100
101
110
111
10*
11*
00*
01*
0**
1**
***
With size 26 missed <=2 HHs
At level 2 missed <=2 HH
Threshold=10
The error for our accuracy estimator for Heavy hitters is below 5% for real traffic traces
Notes: How to estimate missed HHs?
HHH: challenge:
Describe what is HHH
reported ones are the true ones
Dependent on each other
The average error for accuracy estimation is 5% in general and its error reduces as the accuracy increases. For example if the accuracy is above 80%, then the average error is about 1% in our experiments. This is because for higher accuracies, we need more resources. More resources also help to have lower error for accuracy estimation: With lower error we monitor more nodes close to leaves with smaller volume

## Slide 15: Dynamic Resource Allocator
Controller
Heavy Hitter detection
Heavy Hitter detection
Heavy Hitter detection
H
Change detection
Dynamic Resource Allocator
Estimated accuracy
Allocated resource
Estimated accuracy
Allocated resource
Decompose the resource allocator to each switch
  Each switch separately increase/decrease resources
  When and how to change resources?

## Slide 16: Per-switch Resource Allocator: When?
When a task on a switch needs more resources?
  Global accuracy is important
    if bound is 40%, no need to increase A’s resources
  Local accuracy is important
    if bound is 80%, increasing B’s resources is not helpful
  Conclusion: when max(local, global) < accuracy bound
A
B
Controller
Heavy Hitter detection
Detected HH:5 out of 20
Local accuracy=25%
Detected HH:9 out of 10
Local accuracy=90%
Detected HH: 14 out of 30
Global accuracy=47%

## Slide 17: Per-Switch Resource Allocator: How?
How to adapt resources?
  Take from rich tasks (r=r-s), give to poor tasks (r=r+s)
How much resource to take/give?
  Approach: Adaptive change step (s) for fast convergence
  Intuition: Small steps close to bound, large steps otherwise
Additive increase in both AA and AM methods converges slowly when the goal changes
Additive decrease cannot decrease the step size fast to converge to a fixed value
Multiplicative increase and Multiplicative decrease has converges fast
Notes:   If status changed  close to bound
  increase if status is same
  decrease if status changes
  We see higher rejection for HH than HHH, because we over estimate miss HH, underestimate accuracy, use more resources than necessary
  For HHH, we use precision, we don’t have such problem.
  For change detection, we have this problem too.
  We can improve the accuracy of recall, if we assume a model of traffic. If we know the traffic is skewed.
  The results show that

## Slide 18: DREAM Overview
Task object 1
Task object n
DREAM
SDN Controller
2) Accept/Reject
5) Report
1) Instantiate task
3) Configure counters
4) Fetch counters
7) Allocate / Drop
6) Estimate accuracy
Resource Allocator
  Task type (Heavy hitter, Hierarchical heavy hitter, Change detection)
  Task specific parameters (HH threshold)
  Packet header field (source IP)
  Filter (src IP=10/24, dst IP=10.2/16)
  Accuracy bound (80%)
Prototype Implementation with DREAM algorithms on Floodlight and Open vSwitches

## Slide 19: Prototype Evaluation
DREAM prototype
  DREAM algorithms in Floodlight controller
  8 Open vSwitches
Prototype evaluation
  256 tasks (HH, HHH, CD, combination)
  5 min tasks arriving in 20 mins
  Replaying 5 hours CAIDA trace
  Validate simulation using prototype
Notes: Large scale simulation (4096 tasks on 32 switches)
  accuracy bounds
  task loads (arrival rate, duration, switch size)
  tasks (task types, task parameters ex. Threshold)
  # switches per tasks

## Slide 20: DREAM Conclusion
Challenges with software-defined measurement
  Diverse and dynamic measurement tasks
  Limited resources at switches
Dynamic resource allocation across tasks
  Accuracy estimators for TCAM-based algorithms
  Spatial and temporal resource multiplexing
Notes: Future work
  Apply DREAM on the hash-based primitive (Sketches)
  Time-slicing measurement
  Other service interfaces to tasks

## Slide 21: Summary
Software-defined measurement
  Measurement is important, yet underexplored
  SDN brings new opportunities to measurement
  Time to rebuild the entire measurement stack
Our work
  OpenSketch:Generic, efficient measurement on sketches
  DREAM: Dynamic resource allocation for many tasks

## Slide 22: Thanks!