## Slide 1: SDN Scalability Issues

## Slide 2: Last Class
Measuring with SDN
  What are measurement tasks?
  What are sketches? What is the minimal building blocks for implementing arbitrary sketches?
  How do we trade-off between accuracy and space?
  How to allocate memory across a set of switches to support a given accuracy

## Slide 3: Today’s Class
What are bottlenecks within SDN ecosystem?
SDN Controller 2
(FloodLight)
S4
S2
S1
Hub
MacTracker

## Slide 4: Bottleneck 1: Control Channel
TCAM
Switch CPU
13Mbs
35Mbs
250GB
250GB
SDN Controller 2
(FloodLight)
Hub
MacTracker
The switch NIC processes
packets at 250GB
If packets go to CPU,
they uses PCI bus
If packets go to controller,
they uses TCP connection

## Slide 5: Bottleneck 2: TCAM Memory
TCAM
Switch CPU
13Mbs
35Mbs
250GB
250GB
SDN Controller 2
(FloodLight)
Hub
MacTracker
The switch NIC processes
packets at 250GB
If packets go to CPU,
they uses PCI bus
If packets go to controller,
they uses TCP connection
Only stores N flow table entries. Limits number of flow entries

## Slide 6: Bottleneck 3: Controller Server
TCAM
Switch CPU
13Mbs
35Mbs
250GB
250GB
SDN Controller 2
(FloodLight)
Hub
MacTracker
The switch NIC processes
packets at 250GB
If packets go to CPU,
they uses PCI bus
If packets go to controller,
they uses TCP connection
Runs on a mac: only so much CPU & RAM. Limits Apps

## Slide 7: Today’s Class
What are bottlenecks within SDN ecosystem?
  Control Channel
  Controller Server (Scalability)
  Switch TCAM (Number of entries)
SDN Controller 2
(FloodLight)
S4
S2
S1
Hub
MacTracker

## Slide 8: How to Get Around TCAM Limitations
Use the controller
Use a hierarchy of Switches
Place servers/applications/VM wisely

## Slide 9: How to Get Around TCAM Limitations
Use the controller
  Doesn’t Scale --- remember controller has limits
  Too slow --- takes over 10ms to get info to controller
Use a hierarchy of Switches
  Difane
Place servers/applications/VM wisely
  VM Bin Packing

## Slide 10: DiFane
Creates a hierarchy of switches
  Authoritative switches
    Lots of memory
    Collectively stores all the rules
  Local switches
    Small amount of memory
    Stores a few rules
    For unknown rules route traffic to an authoritative switch

## Slide 11: Packet Redirection and Rule Caching
Following packets
Ingress Switch
Authority Switch
Egress Switch
First packet
Redirect
Forward
Feedback:
Cache rules
Hit cached rules and forward
A slightly longer path in the data plane is faster than going through the control plane

## Slide 12: Packet Redirection and Rule Caching
Following packets
Ingress Switch
Authority Switch
Egress Switch
First packet
Redirect
Forward
Feedback:
Cache rules
Hit cached rules and forward
To: bruce
Everything else
To: bruce
To: Theo

## Slide 13: Three Sets of Rules in TCAM
Type | Priority | Field 1 | Field 2 | Action | Timeout
Cache Rules | 210 | 00** | 111* | Forward to Switch B | 10 sec
 | 209 | 1110 | 11** | Drop | 10 sec
 | … | … | … | … | …
Authority Rules | 110 | 00** | 001* | Forward Trigger cache manager | Infinity
 | 109 | 0001 | 0*** | Drop, Trigger cache manager | 
 | … | … | … | … | …
Partition Rules | 15 | 0*** | 000* | Redirect to auth. switch | 
 | 14 |  |  | … | 
 | … | … | … | … | …
In ingress switches
reactively installed by authority switches
In authority switches
proactively installed by controller
In every switch
proactively installed by controller

## Slide 14: Stage 1
The controller proactively generates the rules and distributes them to authority switches.

## Slide 15: Partition and Distribute the Flow Rules
Ingress Switch
Egress Switch
Distribute partition information
Authority Switch A
AuthoritySwitch B
Authority Switch C
reject
accept
Flow space
Controller
Authority
Switch A
Authority
Switch B
Authority
Switch C

## Slide 16: Stage 2
The authority switches keep packets always in the data plane and reactively cache rules.

## Slide 17: Packet Redirection and Rule Caching
Following packets
Ingress Switch
Authority Switch
Egress Switch
First packet
Redirect
Forward
Feedback:
Cache rules
Hit cached rules and forward
A slightly longer path in the data plane is faster than going through the control plane

## Slide 18: Assumptions
That Authoritative switches have more TCAM than regular switches
You know all the rules you want to insert into the switches before hand.
  So your SDN-App you should like Assignment 3
  If your SDN-App is like Assignment2 (Hub), all first packets will still need to go to the controller

## Slide 19: Interesting Questions
What quickly can the authoritative switches install a cache rule into the other switches?
How many cache-rules can the authoritative switches generate per second?
Notes: Should the authoritative switch have any special hardware/software?

## Slide 20: How to Get Around TCAM Limitations
Use the controller
  Doesn’t Scale --- remember controller has limits
  Too slow --- takes over 10ms to get info to controller
Use a hierarchy of Switches
  Difane
Place servers/applications/VM wisely
  VM Bin Packing

## Slide 21: Distributed Applications
Applications have set communication patterns.
  E.g.3-Tier applications.
Insight: traffic is between certain servers
  If server placed together then their rules are only inserted in one switch

## Slide 22: Insight
VM A,B,C talk to only each other
  If you place together you can limit TCAM usage
VM C talks to everyone.
Everyone
VM C
VM B
VM A

## Slide 23: Bin-Packing of VMs
VMA
VMB
2

## Slide 24: Random Placement of VMs
VMA
VMB
2
2
2
2
2

## Slide 25
VMA
VMB
2
2
2
2
2
VMA
VMB
2
Random Placement
Bin-Packing

## Slide 26: Limitations
Some applications don’t have nice communication patterns
  How do you learn these patterns?
Some applications are too large to fit in one rack --- too spread out.